## Slide 1: Reflective Roofing: Concerns, Issues, Precautions & Design
presented by
Thomas W. Hutchinson, AIA, CSI, FRCI, RRC
Hutchinson Design Group, Ltd.
Puget Sound Chapter Meeting
November 7, 2012 Seattle, Washington

## Slide 2: Why Are we here?

## Slide 3: Energy Savings MYTH OR FACT!

## Slide 4: Why Are we here?

## Slide 5: Why Are we here?

## Slide 6: Why Are we here?

## Slide 7: Why Are we here?

## Slide 8: Why Are we here?

## Slide 9: Why Are we here?

## Slide 10: Presentation Quiz….
Water flows down hill?
  True
  False
  Sometimes
  Only on steep slope roofs
Roof warranties are a promise of a leak free roof?
  True
  False
FM 1A-90 is for wind coverage of 90 mph?
  True
  False
A roof material with a UL Class A rating will not burn?
  True
  False
The air over a cool roof is cooler than the air over a dark membrane roof?
  True
  False

## Slide 11: Presentation Quiz
Bonus Question:
Moisture intrusion is the #1 cause of legal concern for Architects?
  True
  False

## Slide 12: Presentation Quiz
Bonus Question:
A ‘Cool’ roof membrane will always save energy?
  True
  False

## Slide 13
More than likely you said, 'A bird in the bush,'! and. ........ if this IS what YOU said, then you failed to see that the word THE is repeated twice! Sorry, look again.

## Slide 14
ALZHEIMER'S EYE TEST
Count every ' F ' in the following text:
FINISHED FILES ARE THE RE SULT OF YEARS OF SCIENTI FIC STUDY COMBINED WITH THE EXPERIENCE OF YEARS...

## Slide 15
ALZHEIMER'S EYE TEST
Count every ' F ' in the following text:
FINISHED FILES ARE THE RE SULT OF YEARS OF SCIENTI FIC STUDY COMBINED WITH THE EXPERIENCE OF YEARS...
HOW MANY ? WRONG, THERE ARE 6 -- no joke. READ IT AGAIN ! .
The reasoning behind is further down. The brain cannot process 'OF'.
Notes: 1/10/2014 8:42:10 AM
CAC-RCI - Jan 14, 2008
15

## Slide 16
More Brain Stuff . .
From Cambridge University ... Olny srmat poelpe can raed tihs. I cdnuolt blveiee taht I cluod aulaclty uesdnatnrd waht I was rdanieg.. The phaonmneal pweor of the hmuan mnid, aoccdrnig to a rscheearch at Cmabrigde Uinervtisy, it deosn't mttaer in waht oredr the ltteers in a wrod are, the olny iprmoatnt tihng is taht the frist and lsat ltteer be in the rghit pclae. The rset can be a taotl mses and you can sitll raed it wouthit a porbelm. Tihs is bcuseae the huamn mnid deos not raed ervey lteter by istlef, but the wrod as a wlohe. Amzanig huh? yaeh and I awlyas tghuhot slpeling was ipmorantt! if you can raed tihs psas it on!!

## Slide 17: Photos of Performing Cool Roofs
TPO
Modified Bitumen
Ballasted
EPDM

## Slide 18: Performing Cool Roofs
TPO

## Slide 19: Performing Cool Roofs
TPO

## Slide 20: Performing Cool Roofs
Modified Bitumen

## Slide 21: Performing Cool Roofs
Ballasted

## Slide 22: Performing Cool Roofs
EPDM

## Slide 23: Performing Cool Roofs
Qualified Roof Inspector
Modified Bitumen

## Slide 24: non-Performing Cool Roofs
TPO
Modified Bitumen

## Slide 25: non-Performing Cool Roofs
Modified Bitumen

## Slide 26: non-Performing Cool Roofs
TPO

## Slide 27: non-Performing Cool Roofs
TPO

## Slide 28: non-Performing Cool Roofs
TPO

## Slide 29: non-Performing Cool Roofs
Modified Bitumen

## Slide 30: non-Performing Cool Roofs
Modified Bitumen

## Slide 31: non-Performing Cool Roofs
Modified Bitumen

## Slide 32: non-Performing Cool Roofs
Modified Bitumen

## Slide 33: non-Performing Cool Roofs
Modified Bitumen

## Slide 34: Today’s Goals
Understand the importance of DESIGN in ‘Cool Roof Systems’
Grasp the importance of understanding and controlling air movement in the success of roof system design
Understanding that air flow into cool roof systems can be detrimental to their long term performance
DESIGN

## Slide 35: Today’s Goals
Learn that buildings have life cycles and that interior moisture levels and air flow into roofing systems will vary
Acknowledge that ‘unintended’ consequences can and will shorten service life
Realize roofs are systems, and as such can NOT be designed as a single component

## Slide 36: Today’s Goals
Assist you in the success of your cool roof system design
Realize that you, as designer, and not the proponents of cool roofs, have responsibility if failure results
That as a ‘Designer’ you are responsible for keeping the water above the top of your roof membrane

## Slide 37: GLOBAL WARMING MYTH OR FACT!

## Slide 38: GLOBAL WARMING MYTH OR FACT!

## Slide 39: GLOBAL WARMING MYTH OR FACT!

## Slide 40: Perfect Cool Roof?
Maybe Not!

## Slide 41: History
LEED promotes under auspices of:
  Potential energy savings
  Urban heat island
    Based on publications by LBL
      Pseudo science?
News Flash
“White Roofs Increase Urban Heat Island Effect”

## Slide 42: News Flash
"There does not seem to be a benefit from investing in white roofs," says Jacobson. "The most important thing is to reduce emissions of the pollutants that contribute to global warming.“
- Mark Jacobson, a professor of civil and environmental engineering at Stanford

## Slide 43: Sustainable Fact
Appropriate design and use of materials within a roof system is required to achieve long-term service life

## Slide 44: Long-term Performance = Sustainability 30+ Years

## Slide 45: Long-Term Performance
Ballasted Roof 30 years old

## Slide 46
Waukegan Public SD 60 - Waukegan, IL - 1986
Sustainability is about long-term Service Life

## Slide 47: Sustainability is about long-term Service Life
North Ashboro Middle School, Ashboro, NC

## Slide 48: Sustainability is about long-term Service Life
Firestone’s first EPDM roof, 31 years and still going

## Slide 50: Warranty
Covers leaks

## Slide 51: Warranty
Not condensation

## Slide 52: The Concern
The cool(er) surface temperature of ‘cool’ membranes results in dew points being reach much sooner than darker membranes and does not provide for a downward moisture drive. Thus the potential for a ‘self drying roof system is lost.

## Slide 53: Learning from Experience
Empirical Evidence of Concern
  Concerns began to arise ±2006
  Mysterious interior moisture
    Dripping on sunny days
      No apparent ponding
      No roof surface deficiencies

## Slide 54: Learning from Experience
Cool roof tragedies
  Chicago and Environs - $15,000,000 in reconstruction of cool roof systems less then 3 years old
  A travesty if you’re an owner
  Remember those proponents
  . . . they paid zip, zero, not-a, nothing
  . . . not even a “sorry”

## Slide 56: Learning from Experience
Physics
Condensation

## Slide 57: Learning from Experience
Roofing 101 – Quiz Question
  What is the most deleterious element within a roof system?
  . . . water

## Slide 58: Self Drying Roof Concept

## Slide 59: Self Drying Roof Concept

## Slide 60: Learning from Experience
Condensation
  Don’t create it!

## Slide 61
Condensation
Notes: 61

## Slide 62
Condensation
Notes: CAC-RCI - Jan 14, 2008
62

## Slide 63
Condensation
Notes: CAC-RCI - Jan 14, 2008
63

## Slide 64: Air Flow: Interior to Exterior Means
Diffusion
Leakage
Positive Pressure
Pressure Gradient
  Energy High to Energy Low

## Slide 65: Learning from Experience
Empirical Evidence of Concern
  Building sealant joints (above cool roofs) experience accelerated deterioration

## Slide 66: Learning from Experience

## Slide 67: Learning from Experience

## Slide 68: Learning from Experience
Empirical Evidence of Concern
  Masonry walls (above cool roofs) experience excessive expansion, resulting in over-compressed masonry control sealant joints, reflection into glass windows, and overheating

## Slide 69: Learning from Experience

## Slide 70: Learning from Experience
Empirical Evidence of Concern
  Roof-to-wall base flashings prematurely deteriorating due to excessive heat aging
  Membrane at high parapet walls, high base flashing prematurely deteriorating due to excessive heat aging

## Slide 71: Learning from Experience
Empirical Evidence of Concern
  Low slope roof reflection on adjacent and/or nearby structures a concern

## Slide 72: Roof System Design Considerations
View of Chase Center on East side of Chase Tower

## Slide 73: Roof System Design Considerations

## Slide 74: Learning from Experience
Empirical Evidence of Concern
  Rooftop mechanical equipment operating with increased inefficiency
    Below promised results

## Slide 75
Roof surface cover range of reflectivity from very white to black

## Slide 76
Temperature rise as a function of roof color

## Slide 77
Data Recorded: 9:00 AM -12:00 PM - 3:00 PM - 5:00 PM
CCM Air Temperature Study - 2011
July 7 thru Aug 16 – Carlisle, PA
Temperature Recorded at ;
(0”) - 10” - 16” - 22” - 34”

## Slide 78: Air Temperatures Above Black & White Roof Membranes
12 Noon - Sunny

## Slide 79
Air Temperatures Above Black & White Roof Membranes
30 Day Average

## Slide 80: Learning from Experience
Owners were receiving less then promised
  Much less

## Slide 81: Learning from Experience
Building owners developed concerns
  Interior dripping created a safety concern, for employees a slip potential was created
    An employee fall could expose the owner to legal liability

## Slide 82: Learning from Experience

## Slide 83: Learning from Experience

## Slide 84: Learning from Experience

## Slide 85: Learning from Experience

## Slide 86: Learning from Experience
Building owners developed concerns
  Wet paper insulation facers support mold growth, endangering employee health
    With mold related employee claims on the rise, owners are frightened

## Slide 87: Learning from Experience
Building owners developed concerns
  Continued wetting of the roof deck at the mechanical fastener penetrations raises concerns for corrosion and the potential loss of wind uplift resistance
    Think of where warranty coverage may lie?

## Slide 88: Learning from Experience
Building owners developed concerns
  Single layer insulation and the use of mechanical fasteners reduces thermal performance up to 15%
    Thermal performance, energy conservation less then promised, a cause for legal remediation

## Slide 89
HEAT LOSS
Notes: CAC-RCI - Jan 14, 2008
89

## Slide 90
HEAT LOSS
Notes: CAC-RCI - Jan 14, 2008
90

## Slide 91
HEAT LOSS
Notes: CAC-RCI - Jan 14, 2008
91

## Slide 92
R-18
7%
7%
R-15
R-18
Stabilized
R-18
R-18
Mechanical Fastener
Joint Voids
3” ISO
2 Layers
1-1/2” ISO
Heat Loss
Major Issues with Cool Roofs
Notes: 1/10/2014 8:42:12 AM
CAC-RCI - Jan 14, 2008
92

## Slide 93
R-18
7%
7%
R-15
R-18
Stabilized
R-18
R-18
Mechanical Fastener
Joint Voids
3” ISO
2 Layers
1-1/2” ISO
Vapor/Air Barrier
Vapor/Air Barrier
Notes: 1/10/2014 8:42:12 AM
CAC-RCI - Jan 14, 2008
93

## Slide 94: Learning from Experience
Building owners developed concerns
  HVAC inefficiencies lead not only to employee discomfort and increased energy costs, but also to performance below that which is often promised
    As a building owner, what would you do?
      Look for someone to pay!

## Slide 95: Learning from Experience
Building owners developed concerns
  Deterioration of building elements requires repeated repairs
    Ongoing level of insecurity and cost

## Slide 96: Learning from Experience Case Study
Investigation found similarities in the roof system
  Building Type: Office and warehouse
  Steel Roof Decks:
    Open flutes at walls, roof curbs, drains
    Non-sealed laps
    Welds burn holes through deck
  No vapor retarder
  One layer of insulation, mechanically fastened
  White single-ply membrane, 3 meters wide, and mechanically fastened

## Slide 97
Investigation found similarities in the building construction
  Interior:
    Open floor to roof deck height ±27’-0”; no ceiling
    Gas fired unit heaters below roof deck
    Concrete floors
  Precast concrete walls
  Open gaps between precast and steel roof deck
Learning from Experience Case Study

## Slide 98: Learning from Experience
Winter Concerns:
  Sliding snow
  Wind driven ice

## Slide 99
Additional Winter Condition Concerns

## Slide 100
Additional Winter Condition Concerns

## Slide 101
Additional Winter Condition Concerns

## Slide 102
Additional Winter Condition Concerns

## Slide 103: Learning from Experience
Cool roof membrane on plywood roof decks
    Low slope attic
    Drywall on underside of rafters
    Batt insulation
    Ineffectual vapor retarder
    Airspace below deck
    Poor venting

## Slide 104
Batt insulation friction fitted into rafter space with 2” gap between vapor retarder and rafter renders vapor retarder ineffective. (Like it was not there!)

## Slide 105
Shopping center with trusses, supporting mold growth in unventilated attic, or interstitial spaces, in approximately 18 years

## Slide 106
Four years after changing to a cool roof, condensation was supporting mold growth, collapsing ceilings and damaging decking

## Slide 107: Learning from Experience
Condensation concerns in ASHRAE Regions IV and above
  e.g. Louisville, St. Louis, Chicago, Milwaukee, Sacramento, CA
Not regulated to original cool roof membrane
  Dayton, OH: Building owner paints black EPDM with acrylic coating in an effort to be green
    Results: Interior moisture intrusion

## Slide 108: ASHRAE CLIMATE ZONES

## Slide 109: Learning from Experience
Mechanically fastened membranes ‘pump’ conditioned interior air into the roof system and below the roof membrane

## Slide 110
Provided courtesy of
NRC / CNRC

## Slide 111: Learning from Experience
It’s a physics problem

## Slide 112: Learning from Experience
Positive interior pressure PUSHES conditioned interior air up into the roof system and below the roof membrane

## Slide 113: Learning from Experience
Warranties DO NOT cover any of the issues discussed

## Slide 114: Learning from Experience
Warranty Amendment

## Slide 115: Learning from Experience
Roofs failed due to poor design
  Not a warrantable concern

## Slide 116: Tenet of moisture drive
Air vapor moves from energy high to energy low
  Warm air wants to move to cooler locations

## Slide 117: Tenet of moisture drive
Air doesn’t care what building you are, how famous an architect you are, or what current environmental talk of the week you are, it does what is wants and it is never good

## Slide 118: Learning from Experience
Concerns both during and after construction
  Design for both
Construction generated moisture
  Gas heaters
  Concrete
  Painting

## Slide 119: Cool roof System Design
We now know the problems and can design for them

## Slide 120: Designing cool roof Single Ply Membrane Systems
“What’s the architect, engineer, roof consultant to do?”
Look – manufacturer’s not included!

## Slide 121: Designing cool roof Single Ply Membrane Systems
Investigation & Analysis Phase:
  Interior Conditions:
    Interior climate and space
      Is a high level of humidity a concern

## Slide 122: Designing cool roof Single Ply Membrane Systems
Investigation & Analysis Phase:
  Snow Considerations:
    Why?
    Cool roof membranes are slick
      Snow moves
        Slides down slope
        Can snap off roof top piping
    Remember: Increased levels of thermal insulation will slow snow melt
      Check roof structure capacity

## Slide 123: Designing cool roof Single Ply Membrane Systems
Investigation & Analysis Phase:
  Snow Considerations:
    Ice and snow will move via wind across roof membrane surface; gravel stops will not necessarily stop this
      A condition which creates a life safety concern

## Slide 124
Additional Winter Condition Concerns

## Slide 125: Vapor Retarders
Three phases of building construction to occupancy to consider
  Construction Period: Construction generated moisture needs to be controlled
  Commissioning: Will the building be flushed? Driving potentially moist air into an unprotected roof system
  Occupancy: This is what most consider, not realizing that by then the roof could be in a failed state

## Slide 126: Air Barriers Now Required by Code
2012 International Energy Conservation Code

## Slide 127: Roof System Design Considerations
Membrane Securement Options:
  Fully adhered
  Mechanically fastened - Caution!
    Air pumping action
  Ballasted

## Slide 128: Roof System Design Considerations
Hutch’s Recommendations:
  ASHRAE zones 4 to 7
    Fully adhered
  ASHRAE zones 1 to 3
    Fully adhered, mechanically fastened, ballasted

## Slide 129: Roof System Design Considerations
Why ballasted?
  UV protection of roof membrane
  Greater energy conservation
  Reduced reflection on adjacent buildings

## Slide 130: Roof System Design Considerations
Decisions must be based on sound engineering principles
. . . So that long-term roof system service life can be attained

## Slide 131: Roof System Design Considerations
Let’s Remember:
Long-term
Service Life
is the
Essence of Sustainability

## Slide 132: Roof System Design Considerations
Good Time to Remember:
  Designers design
  Manufacturers produce products
  Contractors install

## Slide 133: Roof System Design Considerations
Manufacturers can provide information, but it’s the designers “Standard of Care” to design the roof system

## Slide 134: Roof System Design Considerations
Membrane thickness?
  Durability is increased with membrane thickness
  Specify greater thickness for durability
    60 mil or greater

## Slide 136: Roof System Design Considerations
Local installer knowledge
  May determine the best roof system type to specify

## Slide 137: Roof System Design Considerations
Energy Efficiency Requirements
  Code
  Owner
  What is right
  What is required for performance
    Dew points
    Thermal shorts

## Slide 138: Roof System Design Considerations
Energy Efficiency Requirements
  2 layer minimum
    Reduces energy loss
    Reduces air movement

## Slide 139: Roof System Design Considerations
Energy Efficiency
  Think into the future
  Anticipate energy costs 15, 20, 30 years into the future . . . and design for them

## Slide 140: Roof System Design Considerations
Energy Efficiency
  Design with thermal values 50% greater than required today

## Slide 141
Insulation R 144
Notes: CAC-RCI - Jan 14, 2008
141

## Slide 142: Roof System Design Considerations
Energy Efficiency
  Be aware of insulation types and densities
  Specify insulation with 25 psi min. and double coated fiberglass coated facer
  Advent of mechanically attached systems (low installed costs) has resulted in the elimination of cover boards . . . which protect thermal insulation layers

## Slide 143: Roof System Design Considerations
Energy Efficiency
  Calculate dew points
  . . . at weak points
  i.e. joints, perimeters
  WUFI … at weak points

## Slide 144: Designing cool roof Single Ply Membrane Systems
Code Compliance:
  Know what and where to question applicability
    Airports
    Lower, adjacent roofs

## Slide 145: Designing cool roof Single Ply Membrane Systems
Design Parameters:
  Tapered insulation
  Segregate penetrations
  Points of air infiltration

## Slide 146: Designing cool roof Single Ply Membrane Systems
Design Parameters:
  Coordinate with other design disciplines
    HVAC
    Plumbing
      Drains
      Extensions
    Structural

## Slide 147: Designing cool roof Single Ply Membrane Systems
All building components which impinge upon the roof system need to be designed into the roof system
  That is they are to be detailed
  Manufacturer’s details are an absolute minimum and are not typically sufficient

## Slide 150: Construction Documents
Goal: “Communicate to the
contractor your design intent”

## Slide 151: Construction Documents
Detail
Detail
Detail

## Slide 152: Construction Documents
Roof Plan:
  Show all curbs, penetrations, tapered insulation layout
  Tag all details
  HVAC RTUs/Condensers
    Design with tan membranes below
  High Flashing: Design with tan membrane

## Slide 160: Construction Documents
Specifications
  “Job/Project” specific

## Slide 161
Wind damage occurred to roof system along approximately 25% of the western side of the roof.

## Slide 162
Wind damage to roof system along approximately 25% of the western side of the roof, included roof edge dismantling, insulation and membrane debonding.

## Slide 163
Wind damage to roof membrane and insulation; note how the insulation was pulled off the roof deck sheathing boards, which are mechanically attached to the steel roof deck.

## Slide 164
Roof edge sheet metal and plywood that was pulled off the roof edge construction.

## Slide 165
Here you can see where the self-adhering vapor retarder was pulled off the sheathing board.

## Slide 166
Roof membrane has been pulled off the insulation by high winds.

## Slide 167
Note the voids between the two layers of insulation, which allow for air movement.

## Slide 168
The foam adhesive was inappropriately spaced. Note in the photo to the right, the lack of evidence that the adhesive bonded to the insulation board above.

## Slide 169
Inappropriate foam adhesive application. It appears the foam adhesive did not properly rise before setting of top layer of insulation.

## Slide 170
Note how this foam insulation did not bond with the overlaying insulation board.

## Slide 171
Inappropriately bonded insulation boards, note that the foam adhesive in the center portion evidences that the boards were not bonded. It does not appear that the insulation was rolled after installation to assure positive adhesion.

## Slide 172
Observable gaps in DensDeck® sheathing.

## Slide 173
The tan roof membrane observed above was from the original roof installation and was not removed when the original roof was removed. The reroof base flashing was place up below this vertical flange and the two membranes were not sealed, allowing for air movement.

## Slide 175
The self-adhering air barrier at the roof edge perimeter is placed and then rolled to assure full positive contact and adhesion.

## Slide 176
Installation of the prefabricated roof curb alongside the plywood on the interior side of the metal stud wall.

## Slide 177
The nail base insulation is installed and screw fastened to the steel roof deck.

## Slide 178
The nail base in the corners is anchored with screw fasteners at 32 per 4’-0” x 8’-0” board into the steel roof deck.

## Slide 179
The prefabricated roof curb is being anchored to the existing structure at 12” O.C. vertically through the flange into a steel angle (see vertical arrows), 12’ O.C. through the 2x at the top of the curb into the plywood and metal stud cap beyond, and in the center through a linear stiffening rib.

## Slide 180
The arrows are locations where spray foam adhesive needs to be installed.

## Slide 181
All void at the roof edge, between insulation pieces and penetrations were filled with spray foam and trimmed flush.

## Slide 182
Prefabricated Roof Edge Curb: Note the offset at the left for when the steel angle at the roof edge is exposed and the liner (red) 2x stiffing rib.

## Slide 183
The existing metal panels/roof edge waved somewhat (perhaps due to the wind damage). Here the new roof curb has been installed atop the previously installed (white) self-adhering air barrier.

## Slide 184
Installation of 90-mil EPDM in bonding adhesive to the previously installed 2” nail base insulation. The EPDM sheets are being seamed together with 6” seam tape.

## Slide 185
The nail base insulation has been installed with joints staggered over the existing insulation joints and screws fastened through to the steel roof deck below.

## Slide 186
Cut back EPDM membrane to ½” of roof drain clamping ring.

## Slide 187
Overflow Roof Drains: The existing extension rings were removed and two new extension rings installed to accommodate the total insulation height. The existing extension rings were found to be heavily rusted and watertightness was a concern, and thus were replaced. The Foreman indicated new insulation was cut to infill around the new extensions, but that no spray foam was installed.

## Slide 188
Note how nicely the OSB board has been cut around the pipe penetrations, and then the void between pipe and insulation sealed with spray foam.

## Slide 189
Plumbing Vent Flashing Complete: Note the target patch around the penetration, which has been ‘stripped in’.

## Slide 190
Field lap seam, with the self-adhering cover strip applied over it. Lap sealant has yet to be installed.

## Slide 191
The installation of the new 90-mil EPDM roof system is complete.

## Slide 192
The installation of the new 90-mil EPDM is complete. Sheet metal copings have yet to be installed.

## Slide 193
The installation of the new 90-mil EPDM is complete. Sheet metal copings have yet to be installed.

## Slide 194
Plumbing Vents:
Install water block between pipe and premolded boot. Install stainless steel draw band and polyurethane sealant atop premolded boot
[DO NOT use lap sealant].

## Slide 195: Conclusions
Roof system designers would benefit by acknowledging:
  That roofs are systems and that designing a roof system based on a single component (color) is not prudent
  Cool roof surfaces change the physical dynamic of the roof system from one that may be self-drying to one that is not, and as such this needs to be designed accordingly

## Slide 196: Conclusions
Roof system designers would benefit by acknowledging:
  Learn from empirical experiences; do what works
  Understand how building design, use and HVAC systems can impact the roof system
  Use vapor and air retarders to retard/prevent air flow into the roof system
  Understand the phases of building construction and select appropriate vapor retarder so that your roof system reaches its service life unaffected
  Do not expect your roof to do more than provide watertightness and thermal protection

## Slide 197: Conclusions
Roof system designers would benefit by acknowledging:
  The long-term success of your roof system is directly proportional to the quality and knowledge of the roof system designer; heed their advice
  Concerns with cool roof systems will continue to grow until the design profession learns what they are and how to appropriately deal with them
  There is no panacea for all roofing conditions, and a roof system type cannot be mandated

## Slide 198: Recommendations
Design recommendations specific to the design of single-ply membrane cool roof systems for designers who desire to achieve long-term roof system performance:
  Use moisture drive analysis of proposed roof system, such as WUFI, to assist you in design solutions

## Slide 199: Recommendations
  Roof Decks:
    Best: Concrete, which will prevent the movement of air from the interior of the building into the roof system
    Vapor control layers are required on steel and all other air permeable roof decks

## Slide 200: Recommendations
  Vapor Control:
    Concrete or Gypsum Roof Deck
    Vapor Retarder
      Continuous
      Supported
      Unpunctured
      Sealed at penetrations, walls, expansion joints
        If you cant trace it with a pencil it will not work
    Need to be compatible with the roof system and method of adhesion
    Mechanical fasteners cannot penetrate the vapor barrier, studies by the NRC show excessive air movement at the screw fasteners

## Slide 201: Recommendations
  All penetrations through the roof deck and vapor retarder need to be sealed
    Coordination with the various disciplines that create the penetration(s) is required

## Slide 202: Recommendations
  Insulation must be installed in layers with offset joints, and secured to the roof deck to meet the wind uplift requirements
    Offset and open insulation joints and voids at penetrations and perimeters need to be sealed
    Insulation needs to be protected:
      Utilize a cover board to protect the insulation from physical damage and increase wind uplift performance

## Slide 203: Recommendations
  Utilize roof membranes of no less than 60 mils; 80 mils preferred

## Slide 204: Recommendations
  Roof membranes should be fully adhered in place, in lieu of being mechanically attached
    Solvent based adhesive should be used over water based or low VOC adhesives
    Base flashing membranes should be of a tan or similar low reflective membrane

## Slide 205: Recommendations
  Tan or similar low reflective membranes should be used below HVAC refrigeration piping, and in and around roof top cooling units